## Slide 1
Dr. P. G. Umape
Assistant Professor
First Year Engineering Department
Pune Institute of Computer Technology
Unit V
Spectroscopic Techniques Laws of Spectroscopy

## Slide 2
Lambert’s Law:
When a beam of monochromatic light is allowed to pass through a transparent solution, the rate of decrease in intensity of light is directly proportional to increase in thickness of media.
Basic Laws of Spectroscopy
Where, I0 is the intensity of incident light
dI is the small change in intensity
db is the small change in thickness of media
Cuvette
It
I0
Monochromatic light

## Slide 3
Lambert’s Law:
Now integrate the equation with the limits
I = I0 when b = 0 and I = It when b = b
Basic Laws of Spectroscopy
Where, I0 is the intensity of incident light
It is the intensity of transmitted light
b is the thickness of media
k is absorption coefficient for the given wavelength and medium

## Slide 4
Lambert’s Law:
Hence based on the derivation, Lambert’s law can be stated as: The intensity of transmitted light It decreases exponentially as the thickness of absorbing medium increases, for the medium of fixed concentration.
Basic Laws of Spectroscopy

## Slide 5
Beer’s law:
When a beam of monochromatic light is allowed to pass through a transparent solution, the rate of decrease in intensity of light is directly proportional to increase in concentration of solution.
Basic Laws of Spectroscopy
Where, I0 is the intensity of incident light
dI is the small change in intensity
dc is the small change in concentration of media
Cuvette
It
I0
Monochromatic light

## Slide 6
Beer’s Law:
Now integrate the equation with the limits
I = I0 when c = 0 and I = It when c = c
Basic Laws of Spectroscopy
Where, I0 is the intensity of incident light
It is the intensity of transmitted light
c is the concentration of media
k’ is absorption coefficient for the given wavelength and medium

## Slide 7
Beer’s Law:
Hence based on the derivation, Beer’s law can be stated as: The intensity of transmitted light It decreases exponentially as the concentration of absorbing medium increases, for the medium of fixed thickness.
Basic Laws of Spectroscopy

## Slide 8
Lambert-Beer’s law:
When a beam of monochromatic light is allowed to pass through a transparent solution, the intensity of transmitted light decreases with increase in thickness as well as concentration of media.
Basic Laws of Spectroscopy
Cuvette
It
I0
Monochromatic light
Where, I0 is the intensity of incident light
dI is the small change in intensity
dx is the small change in thickness of media
dc is the small change in concentration of media

## Slide 9
Lamber-Beer’s Law:
Now integrate the equation with the limits
Basic Laws of Spectroscopy
Where, I0 is the intensity of incident light
It is the intensity of transmitted light
b is the thickness of media
c is the concentration of media
є is absorptivity constant

## Slide 10
Lambert-Beer’s Law:
‘A’ is called as absorbance
While ‘T’ is called as transmittance
is called as molar absorptivity or molar extinction coefficient
It is the absorptivity for a solution having 1 molar concentration and 1cm path length.
Basic Laws of Spectroscopy

## Slide 11
    Lambert’s law
    Beer’s law
    Combined law/Lambert-beer’s law
    Absorption
    Transmission
    Molar absorptivity/Molar extinction coefficient
Summary