## Slide 1: Zeolite Process/ Cation exchange process

## Slide 2
Student should
Know the zeolite and its structure.
Explain the principle, construction and working of zeolite process.
Explain advantages, limitations and applications of zeolite process.
Learning outcomes

## Slide 3
Zeolite is a complex mixture of metal aluminosilicate
While sodium zeolite is a hydrated sodium aluminosilicate represented as Na2Ze
Sodium zeolite can be written as Nax+[(Al2O3)x(SiO2)yZH2O], Where y>x
Zeolite can also be called as Permutit
Hence zeolite process is also called as permutit’s process or Cation exchange process.
Zeolite process

## Slide 4
It has ability to exchange it’s sodium cation with hardness causing ions present in water.
Based on occurrence sodium zeolite are of two types, Natural and Synthetic zeolite.
Natural zeolite are present in porous rocks
Synthetic zeolite are prepared by fusion of Soda, silica and Alumina.
Synthetic zeolite are powdered and have higher cation exchange properties.
Zeolite process

## Slide 5
Structure of Zeolite:
Zeolite has a hexagonal capillary structure
It consist of large number of Si, Al and Oxygen atoms
These atoms occupies edges of hexagonal capillary
Si is connected to four oxygen atoms
Al is connected to four oxygen atoms
Some times oxygen is shared between Si and Al or two Si atoms
Aluminium tetrahedron bears oxygen with –Ve charge
This –Ve charge is balance by Na+ inside the hexagonal capillary.
Zeolite process

## Slide 6
Principle:
When water is passed through zeolite bed
Due to its ability to exchange cation
Hardness causing cations are exchanged by sodium cation present with zeolite
As hardness causing cations are removed, water is said to be mad soft
Here equivalent amount of sodium ions are given in water.
Zeolite process

## Slide 7
Diagram:
Zeolite process
Hard water inlet
Brine inlet for regeneration
Gravels
Soft water
Regeneration waste outlet
Soft water outlet

## Slide 8
Construction:
The zeolite softener consist of a tank provided with two inlet and two outlet
First inlet allows hardwater to enter in the softener, while second one is used to purge NaCl solution for regeneration.
Generally 10% NaCl solution is used for regeneration
In case of outlet one outlet is used to obtain soft water and second one to drain regeneration waste.
Zeolite process

## Slide 9
Construction:
The tank is also provided with a perforated horizontal plate
The plate provide support for the zeolite bed
On this perforated plate coarse powdered zeolite bed is placed.
Zeolite bed is covered by gravels
Zeolite process

## Slide 10
Diagram:
Zeolite process
Hard water inlet
Brine inlet for regeneration
Gravels
Soft water
Regeneration waste outlet
Soft water outlet

## Slide 11
Ca2+
Ca2+
Ca2+
Ca2+
Ca2+
Ca2+
Mg2+
Mg2+
Mg2+
Mg2+
Mg2+
Mg2+
Zeolite process
Na+
Na+
Na+
Na+
Na+
Na+
Na+
Na+
Na+
Na+
Na+

## Slide 12
Process:
Hard water is allowed to enter in the zeolite softener
Water passes through zeolite bed
As zeolite is having capacity to exchange it’s sodium ions with hardness causing ions present in water, hardness causing ions from water are replaced by equivalent amount of sodium ions.
Na2Ze + CaSO4 CaZe + Na2SO4
Zeolite process

## Slide 13
Process:
As all the hardness causing ions are replaced by sodium ions water is made soft.
Regeneration:
When all the sodium ions from zeolite are replaced by Ca2+ or Mg2+ ion, then zeolite looses it’s capacity of water softening.
Here zeolite is exhausted and can be regenerated by NaCl solution CaZe + 2NaCl Na2Ze + CaCl2
Zeolite process

## Slide 14
Advantages:
Softener is compact in nature and occupies small space.
Hardness upto 10 ppm can be achieved.
Easy to operate and maintain and low operation cost.
Water of any hardness can be made soft, no need to pre-test hardness of water.
Whether the zeolite is exhausted or not can be easily tested with soap solution.
Zeolite process

## Slide 15
Limitations:
Water containing heavy metal ions like Fe2+ or Mn2+ forms permanent zeolite and can not be regenerated.
Hot water slowly destroy zeolite bed hence can not be purified.
Water containing mineral acid destroy zeolite.
Water containing colloidal or suspended impurities may choke zeolite bed hence pre-treatment of water is needed.
Though softening is carried out, equivalent amount of salinity is incorporated by this process.
Process is application only for small scale treatment of water.
Zeolite process

## Slide 16
Applications:
Softening of water
It can be used to remove toxic metal cations or cationic impurities from industrial waste water.
It is useful for reclaiming valuable metal cation from industrial waste water e.g. silver, copper, Cromium, lead etc.
Zeolite process

## Slide 17
What is zeolite? It’s types
Structure of zeolite.
Principle of Zeolite process
Construction and working with diagram
Advantages, limitations and applications of zeolite process
Summary