## Slide 1
Unit III Engineering Materials
Topic: conducting polymers
Dr. P. G. Umape
Department of Applied Science
Pune Institute of Computer Technology

## Slide 2: Learning outcomes
Students will be able to

## Slide 3: Conducting polymers
Eg.: Polyacetylene, Polyaniline, polythiopene
Types: Intrinsic & Extrinsic
Structural Requirement:
Planar & highly crystalline,
Linear
Presence of conjugation (free mobile electrons)
Doping: Polymer has to be disturbed - either by removing electrons from (oxidation), or inserting them into (reduction) into the material.
There are two types of doping:
p-doping: Oxidation with halogen
(positive charge developed on polymer)
n-doping: Reduction with alkali metal
(negative charge developed on polymer)

## Slide 4: Conducting polymers
2(CH)x + 3 I2 2 (CH)x+ I3-
Polyacetylene Iodine p-Doped polyecetylene
2(CH)x + FeCI3 2 (CH)x+ FeCI4- + FeCI2
Polyacetylene p-Dope polyecetylene
(CH)x + Na (CH)x- Na+
Polyacetylene Sodium n-Doped polyecetylene

## Slide 5: Conducting polymers
Synthesis of Polyacetylene
Effect of Temperature:
At -78 °C or below: all-cis PA
At 180 °C or higher: all-trans PA
By Ziegler-Natta Catalyst

## Slide 6: Conducting polymers
Polymerization by Other catalysts
Acetylene
PA
Catalysts:
WCl6/(C6H5)4Sn
WCl6/n-BuLi
MoCl5/ (C6H5)4Sn
Note: These conjugate polymers are usually insoluble in organic solvents of have very low solubility

## Slide 7: Conducting polymers
Durham Method
Isomerization of Polybenzvalene

## Slide 8: Conducting polymers
Properties
  Electrical conductor
  Conductivity increases with doping
  High thermal stability
  Insoluble in solvents

## Slide 9: Conducting polymers
Applications of conducting polymers:
Rechargeable Batteries
As antistatic material
Optical filters
Sensors
In electronics (LED)
Photovoltic cells
Telecommuniction systems
Molecular switches
Solar cell
Light-emitting diodes

## Slide 10: summary