## Slide 1
Unit III Engineering Materials
Topic: Introduction to Nanomatrials
Dr. P. G. Umape
Department of Applied Science
Pune Institute of Computer Technology

## Slide 2: Nanomaterial
Introduction:
Why is nanoscience attracting so much interest?
  The fundamental properties of matter change at the nanoscale.
  The properties of atoms and molecules are not governed by the same physical laws as larger objects, but by “quantum mechanics”.
  The physical and chemical properties of nanoparticles can be quite different from those of larger particles of the same substance. Altered properties can include but are not limited to colour, solubility, material strength, electrical conductivity, magnetic behavior, mobility (within the environment and within the human body), chemical reactivity and biological activity.
  it is the boundary between atoms and molecules and the macro world, where ultimately the properties are dictated by the fundamental behavior of atoms. it is one of the final great challenges for humans, in which the control of materials at the atomic level is possible.

## Slide 3: Nanomaterial
Introduction:
  Definition: These are the materials, whose single unit is sized 1-100 nm at least in one dimension
Classification:
Nanomaterial
Zero dimensional
One
dimensional
Two dimensional
Three
dimensional

## Slide 4: Nanomaterial
Classification:
Accordingly, in zero-dimensional (0D) nanomaterials all the dimensions are measured within the nanoscale (no dimensions are larger than 100 nm). Most commonly, 0D nanomaterials are nanoparticles e.g. Quantum dots.
In one-dimensional nanomaterials (1D), one dimension is outside the nanoscale. This class includes nanotubes, nanorods, and nanowires e.g. Carbon Nano-tube.
In two-dimensional nanomaterials (2D), two dimensions are outside the nanoscale. This class exhibits plate-like shapes and includes graphene, nanofilms, nanolayers, and nanocoatings e.g. Graphene sheet.
Three-dimensional nanomaterials (3D) are materials that are not confined to the nanoscale in any dimension. This class can contain bulk powders, dispersions of nanoparticles, bundles of nanowires, and nanotubes as well as multi-nanolayers

## Slide 5: Thanks!!!