## Slide 1: Topic- Determination of Hardness of Water
UNIT I: WATER TECHNOLOGY
Dr. P. G. Umape
Assistant Professor
Pune Institute
of
Computer Technology

## Slide 2
Learning outcome
Student should understand hardness of water and salts responsible for hardness
Student should be able to calculate hardness of water by EDTA method

## Slide 3
It is the property of water to resist formation of foam with soap
What is Hardness of water?
Why It has ability resist formation of foam
It is the soap consuming capacity of water.
OR
Presence of dissolved salt of Ca2+ and Mg2+
(Carbonate, bicarbonate, chlorides, sulphates and nitrates)
Determination of hardness

## Slide 4: Determination of hardness
Hardness of water can be determined by EDTA titration method
Ethylene diamino tetra acetic acid
N-CH2-CH2-N
CH2COOH
CH2COOH
HOOCH2C
HOOCH2C
N-CH2-CH2-N
CH2COOH
CH2COONa
HOOCH2C
NaOOCH2C
Disodium EDTA have more solubility

## Slide 5: Determination of hardness
Hardness of water can be determined by EDTA titration method
It is a complexometric titration in which EDTA is used as a chelating agent
EDTA hexa-dentate ligand and forms a cyclic complex
Has high affinity towards metal ions,
It forms a stable, colorless 1:1 complex with EDTA
CH2-CH2
N
N
H2C
CH2
CH2
CH2
COO-
-OOC
O=C
C=O
O
O
M

## Slide 6: Determination of hardness
Eriochrome Black –T is used as an
EBT forms weak wine red colored complex with Calcium and Magnesium ions.
Metal-EDTA complex is unstable at lower pH
Formation of metal EDTA complex lowers the pH as H+ is produced during reaction
Hence, titration is carried out at pH 10 using NH4Cl - NH4OH buffer as Metal-EDTA complex is stable and forward reaction is favored.
Indicator

## Slide 7: Determination of hardness
Reactions:
M2+ + EBT M-EBT + 2H+
Pink red
M-EBT + EDTA M-EDTA + EBT
colourless blue
Procedure:
Part-A: Standardization of Na2EDTA by MgSO4
Part-B: Determination of total hardness
Part-C: Determination of permanent hardness
Part-D: Determination of temporary hardness
pH = 10
pH = 10

## Slide 8
Procedure
Take V ml of 0.1 M MgSO4 solution
Fill The burette by EDTA solution
0.0 ml
Add 2 drops of EBT indicator
V1 ml
Part-A: Standardization of Na2EDTA by MgSO4

## Slide 9: Determination of hardness
Procedure:
Part-A: Standardization of Na2EDTA by MgSO4
Take 10 ml of Std. MgSO4 solution
Add 2-4 ml of buffer, and 2 drops of EBT indicator, Solution will have wine red colour
Titrate the solution till permanent blue colour is observed.
Fill the burette with EDTA solution
Calculation : M1V1 = M2 V2
Where M1 = Molarity of EDTA (Z)
V1 = Volume of EDTA at end point (CBR)
M2 = Molarity of MgSO4
V2 = Volume of MgSO4 Solution

## Slide 10: Determination of hardness
Procedure:
Part-B: Determination of total hardness
Take 10 ml of Water Sample
Add 2-4 ml of buffer, and 2 drops of EBT indicator, Solution will have wine red colour
Titrate the solution till permanent blue colour is observed.
Fill the burette with EDTA solution
Hardness of water sample = (Y x Z x100 x 1000) / V mg of
CaCO3 eq.
Where Y= Volume of EDTA
Z= Molarity of EDTA
V= Volume of Water sample

## Slide 11: Determination of hardness
Procedure:
Part-C: Determination of permanent hardness
Boil the same water sample, cool and filter.
Analyze the water sample for hardness,
Obtained hardness will be permanent hardness.
Part-D: Determination of temporary hardness
Finally
Temporary hardness = Total Hardness – Permanent Hardness

## Slide 12: Summary
Hardness is calculated by EDTA method.
EBT is used as an indicator
EBT complex is weak and wine red
EDTA complex is stable and colorless
End point of titration is wine red to blue
The titration is carried out at 10 pH
Formula to calculate hardness
= (Y x Z x100 x 1000) / V mg of CaCO3 eq.