## Slide 1: Numerical on Hardness Calculation
Dr. P. G. Umape
Assistant Professor
Pune Institute of Computer Technology

## Slide 2: Learning outcome
Students should be able calculate hardness of water sample

## Slide 3: Numerical 1
50 ml water sample on analysis consume 14 ml of 0.02 M EDTA, Calculate hardness of water sample.
Solution: Given Volume of water sample (V) = 50 ml,
Molarity of EDTA (Z) = 0.02 M,
Volume of EDTA (X)= 14 ml.
Hardness of water sample = X × Z × 100 × 1000/ V
= 14× 0.02 × 100 × 1000/50
= 560 ppm CaCO3 equivalent

## Slide 4: Numerical 2
100 ml water sample on analysis consume 18 ml of 0.025 M EDTA solution, Same 100 ml water sample after boiling and filtration consume 8 ml of same EDTA , Calculate total, temporary and permanent hardness of water sample.
Solution: Given Volume of water sample (V) = 100 ml,
Molarity of EDTA (Z) = 0.025 M,
Volume of EDTA (X)= 18 ml.
Volume of EDTA after boiling = 8 ml
Total Hardness of water sample = X × Z × 100 × 1000/ V
= 18 × 0.025 × 100 × 1000/100
= 450 ppm CaCO3 equivalent.

## Slide 5: Numerical 2
Solution: Given Volume of water sample (V) = 100 ml,
Molarity of EDTA (Z) = 0.025 M,
Volume of EDTA after boiling = 8 ml
Permanant Hardness of water sample
= X × Z × 100 × 1000/ V
= 8 × 0.025 × 100 × 1000/100
= 200 ppm CaCO3 equivalent.
Temporary Hardness =Total hardness – Permanent hardness
Temporary Hardness = 450 – 200 = 250 ppm CaCO3 equivalent.

## Slide 6: Numerical 3
100 ml of 0.02 M MgSO4 consume 20 ml of EDTA, 100 ml of water sample on analysis consume 6.5 ml of same EDTA solution calculate hardness of water sample.
Solution: Given Molarity of MgSO4 (M1) = 0.02 M
Volume of MgSO4 (V1)= 100 ml
Volume of EDTA (V2)= 20 ml
M1V1 = M2V2
M2= M1V1/V2 = 0.02 × 100/20
M2 = 0.1 M

## Slide 7: Numerical 3
Volume of EDTA (X)= 6.5 ml.
Molarity of EDTA = 0.1 M
Volume of water sample = 100 ml
Total Hardness of water sample = X × Z × 100 × 1000/ V
= 6.5× 0.1 × 100 × 1000/100
= 650 ppm CaCO3 equivalent.