## Slide 1: Determination of Alkalinity
Dr. P. G. Umape
Engineering Chemistry
First Year Engineering Department

## Slide 2
It is the ability of water to react with standard acid
What is alkalinity?
Why It has ability to react?
Due to presence of –OH, CO32- , HCO3-.
–OH + H+ H2O
CO32- + H+ HCO3-
HCO3- + H+ H2O + CO2
What is the reaction?
Based on the nature of anion alkalinity can be classified as
Hydroxide alkalinity (–OH )
Carbonate alkalinity (CO32-)
Bicarbonate alkalinity (HCO3-)

## Slide 3: Effects of Alkalinity
Higher the alkalinity higher will be hardness
Have a bad taste
It causes lime scale to build up on plumbing fixtures and pipes.
Hard water can also create a scum like appearance on clothing and dishware.
Higher alkalinity leads to health effects.

## Slide 4
How to Determine alkalinity?
It can be determined by titration method
Water sample is titrated with standard acid
Two indicators are used
Phenolphthalein
Methyl orange
End point
Pink to colourless
-OH, CO32-
HCO3-
Yellow to orange

## Slide 5: Theory to determine alkalinity
Alkalinity is determined by titrating water sample with standard strong acid.
Two indicators used
Phenolphthalein (Pink to colorless)(pH = 8.2)
Methyl orange (yellow to orange)(pH = 4.4)
Reactions:
-O H + H+ → H2O
CO3-2 + H+ → HCO-3
HCO-3 + H+ → H2O + CO2
Here P = Phenolphthalein, M = Methyl orange
P
M

## Slide 6
Procedure
Take V ml of Water sample
Fill The burette by N/50 Acid
0.0 ml
Add 2 drops of Phenolphthalein indicator
V1 ml
Add 2 drops of Methyl orange
indicator
V2 ml

## Slide 7
Calculation
From the titration following data obtained
Volume of water sample V ml
CBR for Phenolphthalein end point V1 ml
Normality of Acid N/50
CBR for Methyl orange end point V2 ml

## Slide 8
Calculation
Phenolphthalein alkalinity (P) =
Methyl orange alkalinity (M) =
=
V1 X Normality of acid X 50 X 1000
Volume of water sample
ppm CaCO3 equivalent
=
V2 X Normality of acid X 50 X 1000
Volume of water sample
ppm CaCO3 equivalent

## Slide 9
Calculation
Alkalinity | Quantity of OH- | Quantity of CO3-2 | Quantity of HCO3-
P =0 | 0 | 0 | M
P =1/2M | 0 | 2P | 0
P = M | P | 0 | 0
P < 1/2M | 0 | 2P | M-2P
P > 1/2M | (2P-M) | 2(M-P) | 0

## Slide 10: Assignment
Define alkalinity and give its types with example.
What is P alkalinity, Which salts are responsible for P alkalinity?
What is M alkalinity, Which salts are responsible for M alkalinity?
Explain the procedure to determine alkalinity.
How to calculate individual alkalinity?