## Slide 1
Dr. P. G. Umape
First Year Engineering Department
PUNE INSTITUTE OF COMPUTER TECHNOLOGY
Unit IV : Alternative fuel

## Slide 2: Learning Outcomes
Student should know preparation, advantages and a disadvantages of
  Power alcohol
  Biodiesel

## Slide 3: Power Alcohol
When ethyl alcohol (5% - 25%) is used as a fuel by mixing with petrol in I. C. engine then it is called as power alcohol.
Cheapest method to produce the power alcohol is the fermentation method of molasses, starch, carbohydrates on large scale.
As it can be produced from natural feed stock it is a renewable fuel.
The ethyl alcohol required for the I.C. engine should have high purity and must be free from moisture.

## Slide 4: Power Alcohol
Production of Ethyl alcohol:
(C6H10 O5)n
Starch
C12H22 O11
Maltose
Diastage
Maltase
C6H12 O6
Glucose/
Fructose
C12H22 O11
Sucrose
C6H12 O6
Glucose
Invertase
C6H12 O6
Fructose
+
C2H5 OH
Ethyl alcohol
Zymase
C6H12 O6
Glucose/
Fructose

## Slide 5: Power Alcohol
Production of Ethyl alcohol:
As the ethanol is obtained by fermentation process it contains 4.5% water.
But for using the alcohol as a fuel it should be free from water.
The water is removed by dehydrating agent or by distilling alcohol along with benzene.
Advantages of power alcohol
Octane number of ethyl alcohol is 90 and that of petrol is 60, hence it can be used as an antiknocking agent.

## Slide 6: Power Alcohol
Advantages of power alcohol
It reduces dependency on foreign nations for petrol.
It is a renewable source of energy.
It is cheaper than petrol.
The alcohol contains Oxygen atom which helps for the complete combustion and ultimately reduces emission of harmful gases.
Extend the life of engine by reducing overheating.

## Slide 7: Power Alcohol
Limitations of power alcohol
Power alcohol may undergo oxidation to form acetic acid, which corrodes the engine parts.
It has low calorific value than petrol and lowers the power out put.
It has higher surface tension, hence difficult to atomize specifically in colder region and leads to starting trouble.
Alcohol used in IC engine must be free from moisture, but it consist of 4.5% moisture and may lead to problems in engine.

## Slide 8: Power Alcohol
Limitations of power alcohol
As air required for complete combustion of power alcohol is less than the petrol there is a need of engine modification.

## Slide 9: Biodiesel
Biodiesel is a mixture of methyl or ethyl ester of long chain fatty acid.
Biodiesel is prepared by trans- esterification process.
Trans-esterification is a process in which one ester is converted in another.
In this process vegetable oil or animal fat is used as a raw material.
The vegetable oil or animal fat is treated with methanol or ethanol in presence of sodium metal or sodium methoxide / ethoxide as a catalyst.

## Slide 10: Biodiesel
This reaction results in formation of mixture of methyl or ethyl ester of long chain fatty acid called as biodiesel.
With this glycerol is produced as a by product along with small amount of soap.
The by products are water soluble and can be easily removed by washing with water.
As the feedstock used to prepare biodiesel is vegetable oil or animal fat the biodiesel is a renewable source of energy.

## Slide 11: Biodiesel
H2C
HC
H2C
O
O
O
C
C
C
O
O
O
R1
R2
R3
Na/ NaOCH3
3 CH3OH
H2C
HC
H2C
OH
OH
OH
C
C
C
O
O
O
R1
R2
R3
CH3O
CH3O
CH3O
+
Vegetable oil
or Animal fat
Biodiesel
Glycerol

## Slide 12: Biodiesel
Procedure:
Take the non edible oil or animal fat filter it to remove suspended impurities from it.
Add this oil or fat in the reaction vessel and heat it at 11o oC to remove moisture.
Cool to room temperature and add methanol in it(20% of oil or fat).
Then add sodium or sodium methoxide about 2% of oil or fat.
Heat the reaction mixture at 60-70 0C for 1 to 7 h.

## Slide 13: Biodiesel
Procedure:
Time required to complete the reaction depends on vegetable oil or animal fat used for the reaction.
After completion of reaction cool the reaction mass to room temperature, add water to the reaction mass stir well and separate non aqueous layer (Biodiesel).
Dry the biodiesel and add antioxidant so as to avoid oxidation of biodiesel and to impart stability.
The biodiesel can be directly used or blended with diesel as a I.C. engine fuel.

## Slide 14: Biodiesel
Advantages of Biodiesel:
Biodiesel is used as a fuel in diesel engine either mixing with diesel or directly, If 20% of biodiesel is used then it is denoted as B20
It has high Cetane Number 46 to 54
Calorific value of biodiesel is high CV 40kJ/gm
Oxygen content in biodiesel helps for complete combustion, hence it is a clean fuel
Due to its oiliness it acts as a lubricant
It is a renewable source of energy

## Slide 15: Biodiesel
Advantages of Biodiesel:
Biodiesel is sulphur free and non toxic in nature
It is safe to store due to high flash point
Disadvantages of Biodiesel
Biodiesel has low pour point and cloud point hence difficult to use in colder regions.
It strongly adheres on metals and become gummy.
It has dissolving action on rubber hoses and gaskets
Using biodiesel as a I.C. engine fuel may lead to increased price and shortage of vegetable oil.

## Slide 16: Summary
Definition, preparation, Advantages and disadvantages of power alcohol.
Definition, preparation, Advantages and disadvantages of biodiesel

## Slide 17
Thank You