## Slide 1
Dr. P. G. Umape
PUNE INSTITUTE OF COMPUTER TECHNOLOGY
pH metry

## Slide 2: pH metry
pH is the scale to measure H+ ion concentration in an aqueous solution, pH of an aqueous solution can very between 0-14
Mathematically it is expressed as pH = -log[H+]
The analyser which measures pH of a solution is called as pH meter.
The technique which measure the pH of a solution is called as pH metry.
Glass electrode is used to measure the pH of a solution.

## Slide 3: Buffer
It is an aqueous solution of either weak acid and its salt with strong base or weak base and its salt with strong acid, which resist the change in pH of a solution in which it is added, even if small quantity of an acid or base is added in it.
Buffers are of two types
  Acidic buffer: It is a mixture of weak acid and its salt with strong base e.g. CH3COOH + CH3CONa.
  Basic buffer : It is a mixture of weak base and its salt with strong acid e.g. NH4OH + NH4Cl.

## Slide 4: Buffer
Henderson equation
It is used to prepare buffer of specific pH or pH of a buffer solution can be calculated by using Henderson equation.
pH of acidic buffer = pKa + log
pOH of basic buffer = pKb + log
Where pKa and pKb are the negative log10 of the dissociation constant of weak acid and weak base
[Salt]
[Weak acid ]
[Salt]
[Weak base]

## Slide 5: Glass electrode
Principle: When two solutions of different H+ ion concentration are separated by a thin glass membrane then potential difference developed on inner and outer surface of the membrane is proportional to the difference in H+ ion concentration of two membrane i.e. pH of outer solution.
0.1 N HCl
Thin walled Glass bulb
Pt or Ag/AgCl wire
Rubber cap
Glass tube

## Slide 6: Glass electrode
Construction:
It consists of a glass tube.
At the end of this glass tube a special glass bulb is attached.
This glass bulb is having characteristic to exchange H+ ions with Na+ ions present in glass.
The glass bulb is filled with 0.1 M HCl solution as internal reference Solution.
A Pt wire or Silver wire coated with AgCl is Immersed in the inner solution and externally connected to Potentiometer.

## Slide 7: Glass electrode
Construction:
The glass tube is sealed with rubber cap, so as to maintain concentration of reference solution constant.
Glass electrode is represented as follows
Pt,0.1N HCl Glass
Potential on glass electrode is given as
EG = EG o + 0.0591 pH
Where EG o is the potential of glass electrode in a solution of known pH

## Slide 8: Glass electrode
In order to determine the pH of solution, glass electrode is coupled with a reference electrode (Calomel electrode).
These coupled electrodes are dipped into solution of a unknown pH and the cell formed is represented as
Pt| Hg,Hg2Cl2 | Cl- || Test Solution || Glass electrode
EMF of the cell is measured as
E cell = Ecal – EG = 0.2422 – (EG o + 0.0591 pH)

## Slide 9: Glass electrode
Where EG o is the potential of glass electrode in a solution of known pH
          Advantages:
            It is simple to use
            Results are accurate and quick
            Equilibrium is easily attained
            Electrodes do not get poisoned easily

## Slide 10: Glass electrode
          Advantages:
            It can be used in strong oxidizing and reducing solutions
            H+ ions can be determined in presence of other ions
            Turbid, colloidal or colored solutions can be analyzed
            It is portable and compact
            Disadvantages:
              Glass membrane is fragile
              Frequent calibration is required
              Non aqueous solutions does not give accurate results

## Slide 11: Summary
          Definition of pH and PH metry
          Definition of buffer and types of buffer
          Henderson equation to calculate pH of buffer
          Glass electrode principle, construction and working with diagram.

## Slide 12
Thank you