## Slide 1
Unit III Engineering Materials
Topic: Engineering thermoplastics-polycarbonate
Dr. P. G. Umape
Department of Applied Science
Pune Institute of Computer Technology

## Slide 2: Learning outcomes
Students will be able to
Identify specialty polymers
Define engineering thermoplastics
Explain preparation, properties and uses of polycarbonate.

## Slide 3: Specialty polymers
Introduction
  Specialty polymers and resins are proprietary polymers, resins, monomers, and intermediates.
  They include products that are based on proprietary curing technologies or chemistries, or that are designed for specialized applications.
  Specialty polymer provides multifunctional properties
  They have diverse applications that includes water treatment, paper processing, mineral sequestering, textile processing, personal care products, pharmaceuticals, drug delivery, petroleum production, enhanced oil recovery, coatings and inks additives, and sensors.

## Slide 4: Specialty polymers
Introduction
  Specialty Polymers are the class of some High Performance Polymers (HPP), that are designed to meet the critical requirements that engineers face every day in key industries like Plastics, Automobiles, Aeronautics, Smart Devices, Healthcare, Pharmacy, Energy Production and Storage. Specialty polymer includes plastics, polymers, fluids, membranes, smart hydrogels and elastomers.
  If we talk about their “special” performance; it includes exceptional heat resistance and chemical inertness; Strength and toughness; Fatigue and wear resistance; Corrosion, abrasion and weathering protection; Water and stain repellence; Electrical inertness; Fire safety; Biocompatibility; Transparency; colors and many more.

## Slide 5: Specialty polymers
Engineering Thermoplastics
  Thermoplastics?
  Engineering thermoplastics: Plastics having higher thermal as well as mechanical properties than commonly used plastics are called as engineering thermoplastics
  Advantages over common plastics
    Flame retardant and can withstand at 100 oC
    High strength
    Impact resistance
    Stiffness
    Temperature resistance
    They are extensively used in transportation, automotive, electronics, appliance, aerospace, and communications applications.

## Slide 6: Polycarbonate
Synthesis: Reaction carried out in molten state, The product obtained is crystallized after separation of phenol as by product

## Slide 7
Properties:
Has high impact strength
High tensile strength
Transparent having refractive index 1.58
Soluble in organic solvents, alkali
Has heat and flame resistance
Tm=230-250 0C, Tg=145 0C, Sp. Gravity 1.2 gm/cc
Uses:
Used as bullet proof material, vests for windows of houses and vehicles
As insulator in electronics
Used to manufacture domestic ware, helmets, covers of vehicle light
Handles of screw driver, for pliers
To manufacture CD’s, DVD and for housing of apparatus

## Slide 8: summary
Definition of composite materials
Types of composite materials
Composition of Fiber reinforced plastics
Properties of Fiber reinforced plastics
Applications of Fiber reinforced plastics