## Slide 1: Unit IV: Fuel Topic: Hydrogen as a future fuel
Dr. P. G. Umape
PUNE INSTITUTE OF COMPUTER TECHNOLOGY

## Slide 2: Introduction
The fuels we are using now a days are obtained from petroleum, which is a nonrenewable feed stock.
The products of combustion are polluting in nature and are not environment friendly.
Hence there is need to search a fuel that can be obtained from renewable feedstock and greener in nature.
Hydrogen gas seems to the most promising entity in current scenario.
It can be made available from renewable feedstock (water).
The combustion product is water hence greener in nature.

## Slide 3: Introduction
It is non toxic and clean
It has high calorific value
It is used as a rocket fuel
Can be used as a fuel for vehicles
In a fuel cell, directly Hydrogen gas or by using CH3OH as H2 carrier which avoids the need to store H2 under pressure.

## Slide 4: Properties of Hydrogen
Colorless, odorless and insoluble in water.
Diatomic molecule in which two H atoms are joined by strong covalent bond with bond energy 435.9 KJ/mole.
Density is 0.08987 gm/cc at 0° C and 1 atm. pressure, it is 14 times lighter than air.
It burns in air forming water and liberates a large amount of energy, this reaction is often explosive
It reacts with halogen, many metals.
Clean source of energy hence it can replace coal and oil as major source of energy in future

## Slide 5: Production of Hydrogen
Several methods have been reported for the synthesis of hydrogen gas e.g. Steam reforming of hydrocarbon or coal
Electrolysis of water
Water splitting
Photolysis of water using coordination catalyst etc.
Out of all these methods steam reforming of hydrocarbon or steam reforming of coal are the industrially used methods.
Steam reforming is a process in which hydrocarbon or coal is treated with super heated steam in presence of catalyst to produce hydrogen gas and oxide of carbon.

## Slide 6: Production of Hydrogen
Steam reforming of methane or hydrocarbon
The process of steam reforming involves three steps
1) Steam reforming 2) Shift reaction and 3) Removal of CO2
Steam
Steam Reforming
800 0C
FeO catalyst
1 atm
H2+ CO
Shift reaction
Ni/FeO catalyst
370 0C
Steam
H2+ CO2
Feed

## Slide 7: Production of Hydrogen
Steam reforming of methane or hydrocarbon
The process of steam reforming involves three steps
1) Steam reforming 2) shift reaction and 3) removal of CO2
H2+ CO2
Compression and cooling
CO2
H2
95-98% pure
H2

## Slide 8: Production of Hydrogen
Steam reforming of methane or hydrocarbon
iii) Removal of CO2 : Compression & liquefaction of mixture (obtained from Water Gas Shift reaction) to separate Hydrogen gas
The hydrogen gas obtained here is 95-98% pure.
Steam reforming of methane is the preferred process for production of hydrogen

## Slide 9: Production of Hydrogen
Steam reforming of coke/coal
The process of steam reforming involves three steps
1) Steam reforming 2) Shift reaction and 3) Removal of CO2
Steam
Steam Reforming
1000 0C
Ni/FeO catalyst
1 atm
H2+ CO
Shift reaction
FeO catalyst
370 0C
Steam
H2+ CO2
Feed

## Slide 10: Production of Hydrogen
Steam reforming of methane or hydrocarbon
The process of steam reforming involves three steps
1) Steam reforming 2) shift reaction and 3) removal of CO2
H2+ CO2
Compression and cooling
CO2
H2
Pure
H2

## Slide 11: Production of Hydrogen
Steam reforming of methane or hydrocarbon
iii) Removal of CO2 : Compression & liquefaction of mixture (obtained from Water Gas Shift reaction) to separate Hydrogen gas
The hydrogen gas obtained from coal is less & with impurities like H2S, SO2 hence less preferred although cheap.
It can be also purified by scrubbing the mixture through aqueous alkali solution
Or
By treating the mixture with micro porous Pt plate

## Slide 12: Storage of Hydrogen
Difficulties:
Decarburization
Lightest gas (MW:2); Quantity stored less
High cost of compression & energy
Very low Boiling Point -252.60C, difficult to liquefy; high cost of cooling & insulation
Very low Ignition Temp., highly inflammable
Mixture of 2:1 H2-O2 highly explosive
Storage in hydrides requires longer duration & Decomposition requires high Temp

## Slide 13: Storage of Hydrogen
Physical Storage:
Compression – Tanks & cylinders at high pressure
Liquefaction – Cryogenic storage
Adsorption on Carbon nanomaterials – small size,
porous structure(pores of molecular dimension), low density, high surface area
Metal Organic framework (MOF) – crystalline, porous, inorganic-organic hybrid materials
Underground storage

## Slide 14: Applications of hydrogen
As a fuel in Internal combustion engine of vehicles
For preparation of ammonia (Haber’s process)
As a Rocket propellant
4) As a fuel for fuel cells
5) Used in industries:
annealing of metal,
cutting metals,
oxy-hydrogen flame for fabrication